## Slide 1: Lecture 08 – Sequential circuits and key computer building blocks
2017.09.08
What I try to do … is to trace the chain of relationships running from elementary particles, fundamental building blocks of matter everywhere in the universe, … all the way to complex entities, and in particular complex adaptive system like jaguars.
Murray Gell-Mann, physicist

## Slide 2: Announcements
If you wish a DRC environment for midterm
  Provide me your Letter of Accommodation by Wednesday, Sep. 13
  Request DRC evening time for Sep. 21
In consideration of the CS Career Fair there will be no clicker quiz on Monday, Sep. 11

## Slide 3: Announcements
Readily-preventable late assignment submission leniency ends Monday, Sep. 11
  Avoid preventable late submission “sad stories”
    I uploaded Word on time, forgot “PDF!” until too late
    I just totally forgot about the deadline
    I started my upload early, at 11:57:50 p.m.,
    but it didn’t finish until after 11:58:00 p.m.
    because my roommate was binge-watching 8K video
  Help yourself live happy; upload with care, early
    The sad story you prevent will be your own

## Slide 4: Combinatorial and Sequential circuits
Combinatorial circuits implement Boolean functions that are defined by truth tables
  Output = f(inputs); Inputs alone determine outputs
  No ability to retain a history of previous inputs
Sequential circuits implement finite state machines (computers) and are defined by next state diagrams
  Memory of all past sequential circuit inputs is represented by the current state, implemented as bits stored in a register
  Next state = f(current state, current inputs) where f( ) is a combinatorial function and circuit

## Slide 5: Sequential circuit viewed in time
Circuit transitions from one state to the next state, and so on
State i
State i+1
State i+2
f()
INPUTS
at time i
f()
INPUTS
at time i+1
• • •
Time
Register (collection of 1-bit memories) to hold current state
Combinatorial circuit to compute
next_state = f(current state, inputs)

## Slide 6: Improved register component: RS Flip-Flop
RS flip-flop is S’R’ latch controlled by a clock
  If Clock=1, then S and R inverted and sent to latch
  If Clock=0, then latch sees S’=1 and R’=1
Characteristic table
S | R | Q(t+1) | Comment
0 | 0 | Q(t) | No change
0 | 1 | 0 | Reset
1 | 0 | 1 | Set
1 | 1 | ? | Not allowed

## Slide 7: D (data) Flip-Flop: simpler to use than RS F-F
D (data) flip-flop is an RS F-F with R = S’
Characteristic table, whenever clock is high
D | Q(t+1) | Comment
0 | 0 | Reset, or clear
1 | 1 | Set

## Slide 8: Making F-F easier to use in time
So far, flip-flops are sensitive to their input whenever the Clock is at the high logic level
Want to have more precise control of when flip-flop will sense its input
  Prevent F-F from watching the changeable output of a continuously computing combinatorial circuit

## Slide 9: Digital logic signal voltage waveform
Look for a precise marker of time
1) Low level
1) Low level 2) High level
1) Low level 2) High level
3) Rising edge
1) Low level 2) High level
3) Rising edge 4) Falling edge
1) Low level 2) High level
3) Rising edge 4) Falling edge
High band
Low band
10-9seconds per tic mark, for example
Time advances 

## Slide 10: Digital waveform
Rising and falling edges are often drawn in diagrams as if ideally digital, i.e., drawn as vertical lines
See our textbook Figure 2.18

## Slide 11: Flip-flop design using clock edges
Clock waveform
Reg_In_i input ignored
Rising edge loads first D flip-flop with Reg_In_i
Falling edge loads 2nd D flip-flop from 1st
Reg_In_i again ignored

## Slide 12: Edge-triggered, n-bit register
R
S
1-bit
latch
Q0
1-bit
F-F
A1
Q1
1-bit
F-F
A2
Q2
1-bit
F-F
An-2
Qn-2
1-bit
F-F
An-1
Qn-1
Input
Output
V-shape on clock input means edge-triggered Falling clock edge is when newly-stored A bit appears on Q output
A0
Edge-triggered Clock
1-bit
F-F

## Slide 13: Putting together the sequential circuit
INPUTS
State register
Clock ___
f( )
Combinatorial logic
__↑ Clock
Clock ↓____
Clock rising edge ↑ admits Next State bits into State register Clock falling edge ↓ reveals these bits on State register outputs, where these bits are now called the Current State
Falling edge ↓ is a starting gun for the Combinatorial logic, which instantly starts to perform its designed function
Current state 1
Next sate
Current state 2
Output

## Slide 14: The sequential circuit - abstractly
State register
Clock
f( )
Combinatorial logic
This abstraction represents any computer
Current state
Next state
INPUTS
Output

## Slide 15: Sequential circuit & program execution
Conventional programming languages are intended to be executed line-by-line in sequence
Sequential circuit, with its current-state, next-state operation, makes a good match with such programs

## Slide 16: Pointing – a fundamental program action
All of these actions are synonyms
  Name one of N choices
  Select one of N choices
  Point to one of N choices
  Address one of N choices
Programs name, select, point, or addresses frequently
Need a circuit to {name, select, point, address}

## Slide 17: Pointing, visually
Interpret and address, select, name, or point to chosen item
Name
Selection
Address
Pointer

## Slide 18: Circuit for pointing – the decoder
Example: 2-bit number (input) with bits XY and 22 =4 locations to point to: D0, D1, D2, D3
Truth table and circuit; 2 inputs, 22 outputs
X | Y | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 19: Pointing, larger example – 3x8 Decoder
A2 | A1 | A0 | Y7 | Y6 | Y5 | Y4 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Three address bits A2A1A0 name 23 = 8 locations (8 rows)
Eight outputs, Y7Y6 … Y1Y0, each point to 1 distinct location
Notes: Easy SOP circuit

## Slide 20: Lab kit 74HC138 3-to-8 decoder circuit
8 SOP terms
Power to drive many gate inputs
Signals used if wish to link two or four 74138s into larger 4-to-16 or a 5-to-32 decoder
Decoders take in an address, output a selection, a pointer

## Slide 21: Multiplexer/demultiplexer for memory access
Bus – collection of N wires used to carry N bits of data simultaneously from place to place
Circuit to select 1 from 2k data buses
  Multiplexer (Mux): select 1 of 2k input buses and forward selected input to the 1 output bus
  Demultiplexer (Demux): forward the 1 input bus to the selected 1 of 2k output buses
Mux used to read from the pointed to memory location
Demux used to write to the pointed to memory location

## Slide 22: 74251: 1-of-8 mux/demux circuit
8 SOP terms
Data path
Control path
3 pairs of input drivers
Enable’
B1 to B8 are Demux outputs, but Mux inputs
A is Demux input, Mux output

## Slide 23: 1 of 2n multiplexer, more abstractly
Mux
0
1
2n-1
…
…
0
1
n
Input lines; selected from; one is sent to output
Output
Selection Address Pointer
No circuit now; just a box labeled Mux

## Slide 24: Multiplexer also used to choose
Select one of several outcomes
Like a Java switch/case statement
Even more abstract mux symbol used in textbook
Mux
0
1
2n-1
Output
…
0
1
n
…

## Slide 25: 4-bit binary counter using T flip-flops
T flip-flop changes state if T=1, not if T=0
Circuit that counts modulo 2n
Think of this circuit as the code written in hardware that implements the binary counting algorithm (à la CS251)

## Slide 26: Binary counter in lab kit
More complex than previous circuit to include these capabilities
  Can load a chosen 4-bit count value
  Faster, because AND gates are not daisy-chained
  RCO (carry-out) allows n-bit chaining of counters

## Slide 27: Binary counter algorithm, with better initialization, I/O, and optimized performance
Core algorithm plus these user interface and performance capabilities:
  Can load a chosen 4-bit count value
  Faster, because AND gates are not daisy-chained
  RCO (carry-out) allows n-bit chaining of counters

## Slide 28: Summary
Combinatorial circuits implement truth tables
Sequential circuits implement finite state machines
Fundamental sequential circuit is the latch and its more usable cousins, the flip-flops
Key basic computer building blocks include: register, decoder, mux/demux, counter
Hardware can be viewed as the lowest level code in a hierarchy of abstraction