## Slide 1: Lectures 09 – Processors: An overview
2017.09.11
Details create the big picture.
– Sanford Weill

## Slide 2: Assignment for 2017.09.11
Lab 03 – starts this week
HW 03 due Thursday
Read textbook chapter 3
Review your Blackboard scores
  Should see iClicker scores for Sessions 1 thru 6
  If missing iClicker scores, email gba@purdue.edu by noon Friday, 9/15 so we can diagnose and fix
  Lab and HW scores will be appearing gradually

## Slide 3: Components of a computer
Hardware: Digital logic (chapter 2)
  Gates
  Combinatorial and sequential circuits
  Adders, decoders, mux/demux, latch, flip-flops, registers
Data types: Representations for character, integer, and floating point (chapter 3)
Software: Instructions for what to compute
Big prize: Automation

## Slide 4: Automation
User has an App model:
  Start App [software]
  User provides input (optional)
  User gets result(s)
Need
  Hardware to run the App
  App software in a form that the hardware can access without user assistance
  Compare with Lab 02, counting with Clock 4

## Slide 5: Key idea: store program in memory
Registers store bit strings
Bit strings can be interpreted as char, int, float, etc
Let bit strings be interpreted as instructions
Now it is clear that a program can be pre-stored in a computer so that when a user wants a computation performed all that is needed is any required data input
Hardware that stores bits is memory

## Slide 6: Harvard architecture
Idea by Howard Aiken, Harvard physicist, to IBM Nov. 1937
Built by IBM in Endicott, NY and delivered to Harvard in Feb. 1944 as the Mark 1 computer
Has separate memories for program (instructions) and data
Input/output (I/O) to connect to the world
Processor to carry out the computations

## Slide 7: (John) Von Neumann architecture
Developed during his June 1945 train ride from Philadelphia to Los Alamos, NM
He had programmed Mark 1 in August 1944
One memory for both data and program
Same I/O, same processor as Aiken’s “Harvard” design
Notes: Von Neumann clearly better at social media than Aiken (Harvard vs Von Neumann architectures)

## Slide 8: Comparison of architectures
Harvard pro
  Can optimize one memory for storing data, other for storing program
  Can access data and program simultaneously
Harvard con
  Less flexible, memory is physically partitioned
Von Neumann pro
  Cheaper: each $ spent on memory helps store either data or program
  Less secure: hardware cannot distinguish between program instructions and data values

## Slide 9: Range of processor capabilities
Not programmable by user
  Fixed logic processor – circuit is built (“hardwired”) for one function, e.g., traffic signal sequencer
  Selectable logic processor – user can select from multiple hardwired functions, e.g., car with Econo and Sport modes for car’s automatic transmission
  Parameterized logic processor – computes fixed function on variable use input, e.g., programmable video recorder
Programmable by user: programmable logic processor, e.g., laptop computer

## Slide 10: Hierarchical processor structure
A programmable logic processor is often called the CPU (Central Processing Unit)
CPUs today usually comprise a collection of specialized computational engines
  Graphics: accelerates the processing needed for video games; packed as a core, chip, or card
  Pattern: accelerates searches and queries
  AI: accelerates learning algorithms
  Others

## Slide 11: Processor categories
Processors used in a wide variety of roles
  Coprocessor
    Operate with and under control of another, more sophisticated processor
    Implies separately packaged from controlling processor
  Microcontroller
    Used to indicate processor is dedicated to control of a physical system, e.g., electro-mechanical robot joint
  Embedded system processor
    Runs a smart gadget – router, phone, Blu-ray player
  General-purpose processor
    Heart of the personal computer, warehouse computer, smartphone

## Slide 12: Example microcontroller application
Notes: Not like most programs you wrote for CS180 and CS240. Is like the IRC Chat server that you wrote, Spring 2017

## Slide 13: Stored programs
Some memories can be written to only once and then read from many times, called a Read-Only Memory (ROM)
Program for a microcontroller typically is stored in ROM, e.g., automobile engine control computer
Some ROM can be re-written, PROM (programmable ROM)
Embedded system processor often PROM to permit firmware upgrades

## Slide 14: Program translation to machine code
Fetched from memory and executed within the processor

## Slide 15: Processor Fetch-Execute algorithm
At highest level of abstraction, a processor circuit is designed to do this:
Repeat forever* {
FETCH – access the next program instruction
from the location where it is stored.
EXECUTE – perform the action(s) described by the instruction.
}
*Provided the hardware receives power and has not been instructed to halt
Notes: Simple, single purpose computers often do not have a HALT instruction: Apple TV, a microwave oven controller, …
For these computer systems, to stop execution we must remove the power source.

## Slide 16: Storing programs
Program is a sequence of instructions
Memory hardware can be designed as a sequence of locations
Program
Memory
Map instructions to memory locations

## Slide 17: Reading an instruction
Each instruction stored in a memory location
Use multiplexer to point to one location; read instruction (copy its bits); send to processor
Instruction
Instruction
Instruction
Instruction
Location
Location
Location
Location
Location
Location
Program
Memory
Multiplexer
to Processor
Address

## Slide 18: Storing programs
Sequence of addresses sent to multiplexer determines dynamic sequence of instructions
Determining address of next instruction is key
Instruction
Instruction
Instruction
Instruction
Location
Location
Location
Location
Location
Location
Program
Memory
Multiplexer
to Processor
Address

## Slide 19: Clock rate and instruction rate
Fetch-Execute cycle of the processor circuit has a pace set by a clock signal
Number of clock cycles necessary to Fetch and Execute an instruction and the clock cycle frequency depends on
  Speed of memory technology storing operand(s) and result (may be slower than processor circuit)
  Specific instruction to be executed
  Processor circuit design
  History of instruction execution (current state)