## Slide 1: Lecture 10 – From programs to bits
2017.09.13
I have a worm's eye view and a bird's eye view simultaneously, and it's immensely helpful to understand what is happening on the shop floor when you are harnessing many talents and telling an intimate story on a large scale.
– Richard Eyre

## Slide 2: Assignments
Lab 03 – this week
HW 03 due Thursday
Read textbook chapter 3

## Slide 3: Midterm 1 time and location
Thursday, Sep. 21, 6:30pm - 7:30pm
Location - attend the room for your lecture
  LE1: WALC 1055
  LE2: PHYS 112
If you wish a DRC environment for midterm
  Provide me your Letter of Accommodation by Wednesday, Sep. 13
  Request DRC evening time for Sep. 21

## Slide 4: Midterm 1 adjustments
No lecture on Friday, Sep. 22
No GBA office hours on Friday, Sep. 22
Lab sessions week of Sep. 18 unchanged

## Slide 5: Midterm 1 covers
Lectures 01 through 12
Labs 01 through 03
HW 01 through 03
Textbook chapters 1 through 5.5

## Slide 6: Midterm 1 logistics
Test format
  Bring PU ID, several #2 pencils, and an eraser: nothing else allowed at your seat
  TAs and I will not take questions during the exam; re-read carefully and then choose an answer
  Reference materials will be included in exam document
  Exam is closed book, no notes, no calculator

## Slide 7: Midterm 1 format
Test format mostly or entirely multiple choice
More information in next lecture

## Slide 8: Sequential circuit for Fetch-Execute cycle
INPUTS
State register
Clock
f( )
Combinatorial logic
This abstraction represents any computer
Current state
Next state
Output
All bits in memory
External inputs
This abstraction represents any computer executing any program

## Slide 9: Clock rate and instruction rate
The pace of the processor Fetch-Execute cycle is set by a clock signal
Number of clock cycles necessary to Fetch and Execute an instruction and the clock cycle frequency depends on
  Speed of memory technology storing operand(s) and result (may be slower than processor circuit)
  Specific instruction to be executed
  Processor circuit design
  History of instruction execution (current state)

## Slide 10: Processor control: start and stop
Processor circuits are designed to do this: while(true){ Fetch, Execute }
Processors loop forever unless their design includes a halt instruction and until HALT is fetched
Programming consequence:
  either plan for the program to halt using HALT, or
  write the program as an infinite loop
  otherwise program behavior is not predictable
Figure 4.5 door-opening 𝜇controller program is a do_forever loop
Infinite loop for a general purpose computer comes from the operating system

## Slide 11: Starting the Fetch-Execute cycle
Starting is called bootstrap
Many different ways to do it
Simple idea: give all flip-flops a common reset capability
  When power turned on, reset asserted long enough to initialize all registers
  When reset assert period ends, all combinatorial logic will have a known input from which starting Fetch-Execute at a fixed memory location can be assured
  Typical for scenario such as Fig. 4.5

## Slide 12: Starting more complex processors
Laptop and desktop computer bootstrap sequences comprise a chain of steps
At each step a smaller, simpler program loads and then fetch-executes a larger, more complicated program of the next stage
Early stages may involve hardware reset, firmware, loading a Basic I/O System (BIOS)
The final stage loads the operating system from long-term storage into main memory and starts Fetch-Execute cycle

## Slide 13: Booting battery-powered computers
Battery-powered computers (laptops, smart phones) are powered on at the time the battery is installed
The power switch does not turn such computers off, rather the computer enters a very low power mode, operating only a tiny circuit that watches for the device to be “turned on”
  the technical data, “specs,” for my laptop says it can sustain this mode, called sleeping, for at least 1 month
Turning battery-powered computers “on” sends them into a higher power mode that completes the boot up process

## Slide 14: Summary (Chapter 4)
Processors have various types and roles
Processors typically packaged as a single chip
Fetch-Execute never stops, so there must always be a next step in the software a computer runs or else an explicit HALT
High level languages that enhance programmer productivity require considerable translation to be rendered into the language of the processor

## Slide 15: Chapter 5.1 to 5.5 – the instruction set
Program steps in a high level language are called statements
Program steps taken by a processor circuit are called instructions
Statements must be converted (compiled or interpreted) into instructions before a processor circuit can Fetch–Execute
Instructions are
  Direct input to a sequential circuit – must be logic 0 and 1 values represented by low and high voltages
  Represented by strings of bits, binary digits

## Slide 16: Components of a processor instruction
Operation
  Represented by an opcode, operation code (a bit string)
  Opcode is input for decoder that selects, from available combinatorial circuits, the one that performs the desired computation
Operand(s) of the operation
  Number of operands is implied by the operation itself
  Operand type(s) are implicitly declared by operation
  Location of each operand value bit string is immediate, implied, or {named, addressed, selected, or pointed to}
Result of the operation
  Result type is implicitly declared by opcode
  Location to receive result value is implied or {named, addressed, selected, or pointed to}

## Slide 17: Implications of implication
Implication means “it goes without saying,” which means no bits in the instruction bit string are required for this information
Using implication to specify the storage location(s)
  means that if other location(s) are desired for storing operand(s) and/or result(s) then a new opcode is required that implies it is paired with explicit location information
Using implication to specify
  the type of operand(s) and type of result(s) means that a change in data type requires a new operation definition and a new opcode
Notes: Examples: result(s) complex number math
A + B in a C program might be adding integers, might be adding floating point, cannot use same circuit, so the + in C will be translated to different instructions to the processor. The + is OVERLOADED.