## Slide 1: Lecture 12 – Representation (part 2)
2017.09.18
There is always another way to say the same thing that doesn't look at all like the way you said it before. I don't know what the reason for this is. I think it is somehow a representation of the simplicity of nature.
Richard P. Feynman

## Slide 2: Evaluate 1’s complement
What mathematical operations are fast & cheap?
  Negation (for converting X–Y to X + -Y so can subtract with an adder circuit)
  Conversion to/from sign magnitude
  Addition and subtraction automatically generate the correct sign (nice), but
  There is an issue with the output bits from the full adders

## Slide 3: Examples of addition in 1’s comp
2 = 0 0 1 0
+ -3 = + 1 1 0 0
-1 = 0 1 1 1 0
C3S3S2S1S0
• Why show blue C3 = 0? Full adder (FA) will create it. • Is the result correct?
• 1110 sum is negative because sign bit = 1. • What is magnitude of result? Bitwise negate to obtain positive counterpart to see magnitude clearly: |1110|=0001= 1(base 10)
• 1110 = -110 , result is correct
-3 = 1 1 0 0
+ 7 = + 0 1 1 1
4 = 1 0 0 1 1
C3S3S2S1S0
• Full adder (FA) output, |0011| = 0011 = 310 Result is not correct.
• But, connecting C3 to CIN yields 0100, and |0100|= 0100 = 410 • Sum = 0100 = 4 has been corrected.
• For 1’s complement, always add Carry Out of MSB to Carry In to LSB to “correct” the result
Notes: Have an example here 0010 + 1100 (+2 + -3) = 1110 but (-1 + -3 = -4) looks like 1110 + 1100 = 1010 w carry out = -5 w carry out, do carry around for 1010 + 1 = 1011 = -4

## Slide 4: Evaluate 1’s complement
What mathematical operations are not fast & cheap?
  Addition and subtraction need “end-around carry” to achieve correct result
    Connect Carry Out of MSB to Carry In to LSB
    End-Around-Carry increases 1’s complement ripple carry adder propagation delay by 2n gates because the end-arround-carry can propagate to the sum MSB
  Signed addition and subtraction, two very popular operations, are noticeably slower than unsigned addition

## Slide 5: Two’s complement integers
Positive integers use weighted positional
Negative integers formed by inverting all bits of corresponding positive value and adding 1
Example in 4 bits
  0010 represents +2
  1110 represents -2; leftmost bit usable as sign
Quirk: one more negative integer than there are positive integers
Only one representation for zero

## Slide 6
(Again, written in decimal notation)
}
}

## Slide 7: Example: comparing interpretations
Given binary string | Unsigned integer | Sign magnitude | 1’s complement | 2’s complement
0011 | 3 | 3 | 3 | 3
1100 | 12 | -4 | -3 | -4
1101 | 13 | -5 | -2 | -3
1111 | 15 | -7 | -0 | -1
Table shows how given binary strings are interpreted in each data representation
Interpretation expressed as a decimal number
Care taken to show sign for zero

## Slide 8: Evaluate 2’s complement
Negation, a less frequent operation, is slower and more expensive in 2’s than in sign-magnitude or 1’s:
  Invert all bits and then add 1
2’s has only one representation for zero √
2’s high-order bit serves as the sign √
Addition and subtraction generate correct result sign √
Correct numeric result requires no end-around carry √
  thus, 2’s add/subtract hardware circuit is identical to unsigned integer add/subtract hardware circuit √√
Modern computers use unsigned and 2’s complement as their native integer representations (built into the ALU circuitry)
–
√ = good – = bad
Notes: Negation shortcut equivalent to Invert and add 1:
  Starting from the least significant digit, scan leftwards for the first 1 and invert all bits that more significant
  This is equivalent to finding the place where carry propagation stops for the add 1 to the inverted bit string

## Slide 9: Increase # bits, same value: Sign extension
Sign extension: used to increase size of integer representation without changing the value represented, e.g., convert from 32-bit to 64-bit
Value to not change, so LSB position must remain fixed; extend from high-weight bit position
For unsigned numbers, “sign extension” accomplished by adding leading zeros
For 2’s complement extend by copying MSB (sign) bit into the new high-weight bit positions
What hardware is needed to replicate a bit k times?
  A wire with k+1 branches
MSB
k

## Slide 10: Example of sign extension in 2’s comp
2 = 0 0 1 0
+ -3 = + 1 1 0 1
-1 = 0 1 1 1 1
C3S3S2S1S0
• Now sum bits 1111 denote negative result because sign bit = 1, which we expect.
• What is magnitude of this negative result? Bitwise negate and add 1 to obtain positive counterpart to see magnitude easily: (1111)’+1 = 0000 +1 = 0001
2 = 0 0 0 0 0 0 1 0
+ -3 =+ 1 1 1 1 1 1 0 1
-1 = 0 1 1 1 1 1 1 1 1
C7S7S6S5S4S3S2S1S0
• Green bits show sign extension; blue, carry out
• Same sum, -1, in 8-bit format
• To convert 2’s complement to a 2’s comp representation using more bits, extend the sign bit into the additional bit positions
Notes: Have an example here 0010 + 1100 (+2 + -3) = 1110 but (-1 + -3 = -4) looks like 1110 + 1100 = 1010 w carry out = -5 w carry out, do carry around for 1010 + 1 = 1011 = -4

## Slide 11: Binary coded decimal (BCD) integers
Pioneered by IBM for banking
$0.01 in binary is the repeating fraction 0.00000010100011110101110000101000111101011100001010001111010111...
BCD encodes 1 decimal digit per byte
  0x00, 0x01, … 0x08, 0x09
  Bytes 0x0A through 0x0F reserved; standard use is + = 0x0C and – = 0x0D
  Sign-magnitude format, but
  Sign placed last so number of decimal digits within an encoded number may vary: scanning terminates when a sign encountered

## Slide 12: Packed BCD (space efficient BCD)
Packed BCD encodes 2 decimal digits per byte
  0x00, 0x01, … 0x08, 0x09, 0x10, 0x11, … 0x99
  Hex digits 0xA through 0xF reserved; standard use is + = 0xC and – = 0xD
  Note: each nibble (½ byte) holds 1 decimal digit or sign symbol
    Numbers with an odd number of decimal digits can “tuck” sign in after least significant digit in last nibble
    Numbers with an even number of digits will need to be padded to a whole number of bytes using some agreeable definition for the nibble after the sign symbol
  Why packed BCD? Less wasted space than BCD
Notes: Half a byte is a nybble. Who says CS majors don’t have a sense of humor?

## Slide 13: Evaluating BCD
Disadvantages
  Takes more space than unsigned or 2’s complement binary (more bits)
  Hardware circuits for +, –, *, / are somewhat more complex
Advantages
  Can emulate base 10 human math; used in Excel
  Avoids needing a repeating fraction for $0.01

## Slide 14: Overflow and underflow
Overflow means operation result is greater than the maximum representable value; Underflow result is less than smallest representable value
Hardware can generate overflow and underflow signals
  Carry out from MSB is an overflow signal
Overflow/underflow can signal software to execute special case code or throw an exception

## Slide 15: Storage order for bits and bytes
Storage order of bits within a byte is handled by hardware and usually completely hidden from software
Memory is most often byte-addressed, so byte order is exposed to software
How multi-byte items span bytes is a HW design choice
  Affects connection (wires) between storage and ALU
  Informs how to send/receive data via a network
I/O done via memory, so byte order of multi-byte items may need translation between communicating computers
Byte order visible and important to the programmer
Notes: Internal wiring does not affect programmer.

## Slide 16: Big endian and Little endian
There are two multi-byte storage schemes named by which “end” of the multi-byte item is first
We first imagine that memory is read from lowest address number to highest address number, then
  Big endian – most significant byte, “Big” byte, comes first, i.e., placed in lowest numbered memory location of the locations spanned (“Big” end appears first when reading memory), remaining bytes follow in MSB to LSB order
  Little endian – the reverse of Big endian; least significant byte, “Little” byte, placed in lowest address followed by remaining bytes in LSB to MSB order (“Little” end first)

## Slide 17: Example and comparison
Consider 0x00C0F380 = 0x 00 C0 F3 80 = 0b0000 0000 1100 0000 1111 0011 1000 0000
Most significant byte
Least significant byte
Memory address | Byte at given location | 
 | Little endian | Big endian
0x00000000 | 1000 0000 | 0000 0000
0x00000001 | 1111 0000 | 1100 0000
0x00000002 | 1100 0000 | 1111 0011
0x00000003 | 0000 0000 | 1000 0000
Addresses arbitrarily start at 0x00000000. Memory addresses are accessed in the arrow-indicated sequence.

## Slide 18: IEEE Floating Point Standard
IEEE 754 standard for floating point (FP) specifies
  FP format specified at the bit-string level: transfer of FP data between computers requires no format conversion
  Results produced as if using infinitely precise arithmetic then rounded according to specific rules
  Exceptional conditions (overflow, divide by zero, etc.) can propagate through a computation in a benign manner, then be handled by software in a controlled fashion
FP software and data run unmodified on diverse computers
Better environment for numerical computation
  Encourages standard elementary functions
  Provides better support for diagnosis of runtime anomalies
Issues: Addition of FP numbers is not associative, etc.
  See CS courses in numerical analysis / scientific computation for details

## Slide 19: Reasons for IEEE Floating Point Standard
FP data could not be directly exchanged between different computers because formats were incompatible
FP software could not be easily ported from one computer to another
Unsigned integers and 2’s complement have only one implementation given a fixed number of bits
But # of bits does not define a FP representation, so a standard is needed; IEEE developed it in 1985.
William Kahan (UCBerkeley) received ACM Turing Award for his work on IEEE FP Standard in 1989

## Slide 20: Floating point numbers
Floating point (FP) mimics scientific notation ± a x rb where a =significant digits, b order of magnitude, r is radix or base
Example: Avogadro’s number 6.023 x 1023
  +6.023 is the significand or mantissa; shown here with 4 significant digits (non-padding zero digits)
  23 is the exponent
  10 is the radix, or base
  Normalized form: b is chosen so that 1 ≤ |a| < r
Binary is degenerate case for normalization, 1 ≤ |a| < 2, so most significant digit must be 1

## Slide 21: Precision and Range
Precision is the resolution of a representation system
  Defined as the minimum difference between any two representations
  For 32-bit integers, precision is ±1 (± 20)
  For IEEE FP precision is equal to ± the weighted positional value of the mantissa LSB
Range is a pair of numbers (smallest, largest) that bounds all representable numbers in a given system
  For 32-bit unsigned integers range is (0, 232-1)

## Slide 22
MSB
30
(8 bits)
(23 bits or about 7 decimal digits)
↑
sign
Next-to-MSB
22
(11 bits)
(53 bits or about 16 decimal digits or 1 part in 1016)
Precision is determined by the number of digits in the mantissa; Range by number of digits in the exponent. Assume a fixed word length. Then moving the dividing line between the exponent and mantissa fields left decreases range and increases precision. If moved right, then the opposite is true. This is the range/precision tradeoff for FP.
LSB
LSB
←|→
|
less range←|→less precision
Notes: A lot like playing around with the size of the fields in instructions to gain or loose expressivity w.r.t. # registers, range of offset, etc.

## Slide 23
MSB
30
(8 bits)
(23 bits or about 7 decimal digits)
↑
sign
Next-to-MSB
22
(11 bits)
(53 bits or about 16 decimal digits or 1 part in 1016)
STORAGE REPRESENTATION of Floating Point is depicted above.
Sign is a 1-bit field identical in definition to sign-magnitude format.
Exponent is an integer, but has a new representation scheme.
Mantissa is stored without its MSB (most significant bit)
ALU hardware takes advantage of this deeply thought out scheme.
LSB
LSB

## Slide 24: Range of values in IEEE floating point
Single-precision (32-bit format) range is 2-126 to 2127
Double precision (64-bit format) range is 2-1022 to 21023
Approximately equivalent decimal ranges 10-38 to 1038 and 10-308 to 10308
Exponents for equal values expressed in radix 2 versus 10 are in the ratio of ln 10 / ln 2 ≅ 3.3
In other words, 3.3 bits equal the range of 1 decimal digit

## Slide 25: IEEE FP implementation details
Format: Sign | Biased exponent | Mantissa with hidden 1 MSB or s|E|M
Sign field definition same as ever: 0 means + 1 means –
Notes: Yada, yada, yada

## Slide 26: IEEE FP implementation details
Exponent representation: Biased unsigned integer
Bias makes comparing two FP numbers much easier
  Range of 8-bit exponent e is –127 to +127 in sign magnitude
  Represent e as unsigned integer E = e+Bias where Bias = 127
  Thus, 0 ≤ E ≤ 255
  Consider FP numbers x1 = s1E1M1 and x2 = s2E2M2
  Let ⦁ denote concatenation of bit fields and interpret the bit strings s1⦁E1⦁M1 and s2⦁E2⦁M2 as sign magnitude numbers
  FP numbers x1 > x2 if and only if s1⦁E1⦁M1 > s2⦁E2⦁M2
  Biased exponents permits comparing FP numbers using integer compare hardware

## Slide 27: IEEE FP implementation details
Normalized mantissa has one significant digit to the left of the radix point
In binary, this digit must be 1, no other choice
Mantissa form is always 1.m22m21…m1m0 so
  Neither FP registers nor memory store the 1
  ALU inserts this 1 bit into each incoming operand, implements this MSB within ALU circuits, then strips it from each result on the way to storage
  Compute with one more bit of precision with no memory cost
  Called the hidden bit

## Slide 28: IEEE FP support for diagnosis of runtime anomalies
Smallest & largest biased exponent values reserved for special uses (and Mantissa MSB=0 in these uses)
  ±0 written as Sign= 0 or 1, E=0, & Mantissa m bits are all 0s
  de-normalized number, used for gradual underflow, written E=0 and Mantissa m bits ≠0, except Mantissa MSB=0
  ±∞ (± overflows are set to ±∞) written as Sign= 0 or 1, E=255, and m bits =0
  Not a Number (NaN) written E=255 & m bits ≠0
    Example computations that have a result of NaN: 0/0 , x+∞ , √-x , > or < applied to unordered operands

## Slide 29: IEEE FP support for low noise computation
Rounding modes are crucial to retain precision
Inaccurate rounding may inject noise into a computation: result = true value + error
Rounding modes in IEEE 754 FP
  Round to nearest: As if computation was done with infinite precision (only slightly hard to do; this is the default mode)
  Round towards +∞, round towards –∞
  Round towards 0 (simply drop some number of least significant digits, a.k.a. truncation)

## Slide 30: Example interpretation of FP
Interpret the following bit string in IEEE FP, then write its value in decimal scientific notation
1100 0001 1111 0000 0000 0000 0000 0000
1 10000011 11100000000000000000000 (sEM)
Recalling hidden 1, three IEEE FP fields literally say – 131 1.11100000000000000000000 which is -1.111 x 2131–127 = -1.111 x 24

## Slide 31: Conversion between bases
Normalized, weighted positional form is d0r0 + d-1r-1 +…+ d-jr-j x rB = d0.d-1…d-j x rB
Denormalize to obtain exponent=0
20 = Y0 for any Y a positive integer, so
  shift mantissa binary point to be compatible with 20
  now can replace base 2 with base Y as Y0
  then convert mantissa from base 2 to base Y and re-normallize
Example: -1.111 x 24 = -11110.0 x 20 = -30.0 x 100 = -3.0 x 101

## Slide 32: Example decimal scientific to FP
What bit string represents -9.175 x 101 in IEEE FP?
Step 1: determine sign bit Sign = –
Step 2: express -9.175 x 101 using x100: 91.75 x100
Step 3: convert integer & fraction of 91.75 to binary 1011011.11 x100 or, equally, x20
Step 4: normalize binary rational number and use 2a 1.01101111 x 26
Step 5: compute E=e+Bias=6+127=133= 10000101
Step 6: strip mantissa of MSB 1. and assemble fields 1 10000101 01101111000000000000000 regrouped 1100 0010 1011 0111 1000 0000 0000 0000 in hex 0x C 2 B 7 8 0 0 0 or OxC2B78000

## Slide 33: Steps in IEEE floating point ADD and SUB
Align mantissas of operands (shift left or right)
Add or subtract mantissas as usual
Normalize mantissa of result (shift again)
Round mantissa of result
Check for overflow or underflow and other runtime anomalies (override bits in result as required) Quite different from and more complex than integer addition and subtraction

## Slide 34: Summary
There are many representational forms
All programmers can expect to work with character, integer, and floating point data representations
Some programming tasks benefit from specialized representational forms (BCD, etc.)