## Slide 1: Lecture 30 – Memory system design
2017.10.30
Nothing is more responsible for the good old days than a bad memory. – Franklin Pierce Adams

## Slide 2: Assignment for today
Reading chapters 10 through 12
HW08 due Thursday, 9pm
  Solution revealed at 9:02pm
  Submit early
Thursday office hour change, now 3pm to 6pm (starting 1 hour later)

## Slide 3: Announcements
Midterm 2 will be discussed Wednesday
Lab 07 due this week
Lab 08 will issue next week

## Slide 4: Fetch-Store paradigm
All memory technologies provide fetch (read) of a bit string from memory bit_string  memory[address]
Writable memory technologies provide store (write) of a bit string to memory memory[address]  bit_string

## Slide 5: Memory organization
A memory controller connects a processor to a memory unit
Design of controller depends on the technology of the physical memory, e.g.,
  SRAM controller is minimal: SRAM cell is two inverters, logic gates, same technology as processor
  Flash controller is very complex: storage cell wear leveling, neighbor read charge drain compensation, etc.

## Slide 6: Parallelism in interface to memory
Parallel interface used between processor and memory
Interface is called a bus

## Slide 7: Steps in a memory request
Processor
  Presents request (read or write) to controller
  Waits for response
Controller
  Translates request into signals for physical memory
  Responds to processor as quickly as possible
  Prepares memory for next request
  Writes to memory are often buffered
    Processor places address and data in a queue
    Processor can request writes frequently, without stalling on slow memory writes, unless queue is full

## Slide 8: Memory transfer size (word size)
Number of bits, N, transferred to processor from memory simultaneously; determined by bus implementation (designer choice)
N is the word size, or word width, and is typically: 16, 32, and 64 bits
Larger words increase performance
Important to programmers
Word size is a quick way to characterize the performance of a computer; larger corresponds with faster, because more hardware parallelism

## Slide 9: Physical memory address & organization
Each physical memory address corresponds to a word
Physical memory is organized as an array of words (more parallel than an array of bytes)
Hardware reads or writes an entire word at a time, to improve performance

## Slide 10: Byte addressing and translation
Byte addressing
  View of memory presented to the processor
  Each byte of memory is assigned an address
  Convenient, traditional for programmers
  However, underlying hardware uses word addresses (more parallel, higher performance)
Memory controller
  Translates byte addresses to word addresses

## Slide 15: Aligned objects in memory
Designing for flexibility or performance when fetching multibyte and 2k-byte objects
  Flexible: first byte of object can be at any byte address
  Performance: first object byte should be aligned with the first byte of a physical word of memory
  If object size is not a multiple of memory word size then may pad the object to make object size be a multiple of the word size

## Slide 16: Measures of memory size
Some types of memory are naturally constructed in power-of-two capacities
  210 kB, 220 MB, 230 GB, 240 TB, 250 EB, 260 PB bytes are
  One Kilo-, Mega-, Giga-, Tera-, Exa-, Peta-byte (old)
  210 kB, 220 MB, 230 GB, 240 TB, 250 EB, 260 PB bytes are
  One Kibi-, Mebi-, Gibi-, Tebi, Exbi-, Pebi-byte (SI, new)
Some memory types are not: e.g., hard disks
  Capacity is measured using powers of ten
  10000 = 1 kiloByte, 10002 = 1 MegaByte, 10003 = 1 GigaByte, 10004 = 1 TeraByte, 10005 = 1 ExaByte, 10006 = 1 PetaByte byte
Notes: A 64-bit byte-addressed address space holds 16 exbibytes of information.
A gram of DNA can theoretically hold 455 exabytes.[10]

## Slide 17: Increasing physical memory performance
Make memory hardware more parallel, so perform more accesses simultaneously
  Memory banks – harder for programmer to realize the performance potential
  Memory interleaving – easy to exploit in code if you understand the favored patterns of access

## Slide 20: Stride and interleaved memory
Stride is the memory address increment from access to the next
Stride determines when a given interleaved memory module will be next accessed
Desire: do not access a module again until all stall clock cycles for that module have expired
Basic design is to make “Stride of 1” have no stalls
  Achieved when there are at least as many memory modules as there are clock cycles of latency between two consecutive accesses to the same module
Big design question: What other stride values and module numbers combinations have no stalls?

## Slide 21: Interleaving and cyclic group generators
Best constant strides are those with a pattern of memory access that returns to a module only after a delay ≥ module latency
Such strides fully hide the stall cycles of each module with useful accesses to other modules
Module names, (0, 1, 2, …, 2logN-1), and addition modulo 2logN form an algebraic structure called a cyclic group
A generator is a group element that when used repeatedly with the operation will generate all group elements; order of production is immaterial
“Stride = 1” is a generator; any others?

## Slide 22: Explore potential group generators
Code that tries all stride values for (i = 0; i <= 1023; i = i + j) { array[i] = array[i] + 7; }
j=1 gives i=i+1 and stride=1; j=2, stride=2; …
Assume 3 clocks of stall after memory chip access and 4 interleaved modules
j=2 generates which cyclic group elements?
  i=0 so first access is array[0] in module 0, then i=i+2,
  Next access is to array[2] in module 2, then i=i+2,
  Next access is to array[4] in module 0; access pattern set
  j=2 NOT a generator; modules 1 & 3 not accessed
  J=2 does not hide all stalls for this memory design

## Slide 23: Content addressable memory (CAM)
Content addressable memory is also called associative memory
Has “slots” of N bits where N is usually tailored to exactly the need rather than always a power of 2 bits or bytes
CAM does not use pointers for access, instead
  Presented with a key for matching with content
  Hardware simultaneously tests for key match at every bit in CAM, performing a search in fixed, constant time, O(1)
  Result is index of slot(s) where value found

## Slide 24: CAM characteristics
Expensive hardware; each storage bit requires
  Drivers to fan out key bits to all comparators in all slots, e.g., key_bit_i XNOR slot_bit_i for all bits 0 ≤ i ≤ N-1
  For each slot, tree of k-input AND gates to AND the N XNOR bitwise comparison results into a Slot_Match signal
  Circuitry to sequence the readout of all matches
Expensive operation
  on every search, all of the circuitry switches at once: huge power surge
  big wires needed to distribute Vdd and ground
  big heat pulse within the chip

## Slide 25
All bit positions throughout the array are compared to their corresponding key bit simultaneously. Massively parallel design yields single clock cycle identification of matches.

## Slide 26
Route
…
Field(s) associated with each CAM entry
CAM search can return associated information in 1 cycle; used to match IP number with its forwarding information in internet routers.

## Slide 27: Ternary CAM (TCAM)
Variation of CAM that adds partial match searching
Each bit in slot can have one of three values
  Zero
  One
  Don’t care
TCAM ignores “don’t care” bits and reports match
TCAM can either report
  First match
  All matches (indicated using a bit vector)

## Slide 28: Summary
Physical memory
  Organized into fixed-size words
  Accessed through a controller
Controller can use
  Byte addressing when communicating with a processor
  Word addressing when communicating with a physical memory
To avoid arithmetic, use powers of two for
  Address space size
  Bytes per word