## Slide 1: CS 250 Lecture 31 – Memory hierarchy
2017.11.01
We Can Remember It for You Wholesale
by Philip K. Dick
Appeared in the April 1966 edition of
The Magazine of Fantasy and Science Fiction

## Slide 2: Why a hierarchy? Hardware reasons
Memory technologies have widely varying
  Access times (usually quite complex to describe)
  Cost per bit
  Density (bits/per unit volume)
  Power consumption
  Et cetera, et cetera, et cetera
No one technology can truly satisfy even two of the three memory goals: Fast Cheap Large

## Slide 3: Why a hierarchy? Software reasons
During long intervals, meaning “for many, many CPU clock cycles” a program typically will access only a small fraction of its instructions and data
This tendency is called program locality
Program locality has two dimensions
  Space, or the range accessed addresses, and
  Time – “for the next N clock cycles”
If a program “locality” fits in a small but fast memory, then, for a while, fetch and store are FAST

## Slide 4: 90/10 Program Locality Rule
For many programs, about 90% of the instructions executed dynamically, that is, about 90% of the instructions appearing in the program execution trace, come from just 10% of the program source code
So a fast, small, thus affordable cache memory need only contain about 10% of a program to deliver fast performance on 90% of the executed instructions of a program
Gene Amdahl says “I’m lovin’ it! 💝 ”

## Slide 5: Memory hierarchy concept
Build multiple levels of memory spanning a wide range of speeds (costs) and sizes
Each level maps addresses from a slower, larger memory to a smaller, faster memory higher in the hierarchy
Goal: average cost almost as low as the per bit cost of the cheapest level, yet an average speed almost as fast as the fastest level
Goal can be achieved much of the time because of Program Locality of Reference
We can remember it, wholesale
Notes: In the first bullet, why are speed and cost shown as synonyms? Because people pay for performance. Memory is priced mostly on speed and not so much on cost of manufacture.

## Slide 6: Portrait of the memory hierarchy
Register file
L1 (level 1) cache
L2 cache
L3 cache
Main memory
Disk(s) and/or SSD
Remote storage – remote in time
and/or location (e.g., the “Cloud”)
As memory technologies come and go, the layers in the pyramid change. Width of layers is very much NOT to scale with respect to their capacity.
 Part of the processor circuit
 Top of hierarchy accessed by fetch and by LOAD/STORE instructions
 Slower than L1, larger, cheaper
 Slower than L2, larger, cheaper
 Lowest level accessed indirectly by fetch or LOAD/STORE
 Permanent storage of code and data
Movement of bits between these hierarchy levels is managed entirely by hardware
Movement of bits in/out of this level managed by Operating System
Movement of bits between registers and L1 is by LOAD/STORE instructions
Movement of bits in/out of this level managed by various means
 Various uses

## Slide 7: Typical memory hierarchy values
Level | Size in bytes | Typ. access time (ns)
64 64-bit Registers | 512 | 0.25
L1 cache (64 KB) | 65,536 | 1
L2 cache (2 MB) | 2,097,152 | 3
L3 cache (8 MB) | 8,388,608 | 15
DRAM (4 GB) | 4,294,967,296 | 60
Hard disk (1 TB) | 1,000,000,000,000 | 10,000,000
Archive (10 PB) | 10,000,000,000,000,000 | 100,000,000,000
Number of digits is logarithmic with respect to magnitude
Nanoseconds have no visceral meaning
So does the above really speak to us?
Let’s linearize and “visceralize” and try that out.
Notes: Nanoseconds have no visceral meaning: You might seriously say “That was the longest second of my life” but you never say seriously “That was the longest nanosecond of my life!”

## Slide 8: Typical values, linear & familiar scales
Level | If 1 byte = 1 millimeter, capacity as “distance” is | If 1 ns = 1 second, one access takes
64 64-bit Registers | From elbow to fingertips | 0.25 sec
L1 cache (64 KB) | Here to PHYS bus stop | 1 sec
L2 cache (2 MB) | Far bank of the Wabash | 3 sec
L3 cache (8 MB) | East a bit beyond I-65 | 15 sec
DRAM (8 GB) | From here to Naples, Italy | 1 min
Hard disk (1 TB) | 2.5x distance to Moon | ~1 semester
Archive (10 PB) | 1.4x to Pluto or 0.001 ly | 3,169 years
Notes: Print out bytes in a font 1 mm tall??????

## Slide 9: Memory sizes to scale: 1 byte = 1 mm
1 TB hard disk

## Slide 10: Memory sizes to scale
Azimuthal equidistant map for KLAF (Purdue University airport)
1 TB hard disk
8 GB DRAM
Notes: This is the map your fellow Boilermakers are learning as they fly overhead so that can navigate our planet.
Abū Rayḥān Muḥammad ibn Aḥmad Al-Bīrūnī was first to write about this type of map.
Properties: (1) all points are at proportionately correct distances from the center point and (2) all points are at the correct direction, or azimuth, from the center point.
All shortest paths from KLAF to anywhere are radial, straight lines.

## Slide 11: Memory sizes to scale
1 TB hard disk
8 GB DRAM
8 MB L3

## Slide 12: Memory sizes to scale
1 TB hard disk
8 GB DRAM
8 MB L3
2 MB L2
64 KB L1
512 Bytes
Notes: This is the map your fellow Boilermakers are learning as they fly overhead so that can navigate our planet.
Abū Rayḥān Muḥammad ibn Aḥmad Al-Bīrūnī was first to write about this type of map.
Properties: (1) all points are at proportionately correct distances from the center point and (2) all points are at the correct direction, or azimuth, from the center point.
All shortest paths from KLAF to anywhere are radial, straight lines.

## Slide 13: Hierarchy level extremes
Highest level: registers, yes but
  Special level because movement into and out of this level is triggered by the user program via load and store instructions
Lowest level: slowest and largest memory that is considered part of the computer
  Today, most often a disk; tomorrow, Flash?
  Could be a robotic tape library, though
  Could be cloud storage

## Slide 14: Assignment
Read text chapter 13 on virtual memory
Read ahead chapters 14, 15 on input/output

## Slide 15: CS250 Lecture 32 – Cache
2015.11.03
Some computers run my programs. I think they're ok.
If they don't run my programs quickly, I just walk away.
They just read and write DRAM? Then they can't have my bytes.
(That's right!)
Computers with an L1 cache are always “Mr. Right.”
with apologies to Madonna - Material Girl (1985)
Notes: https://www.youtube.com/watch?v=6p-lDYPR2P8 Official music video for Material Girl.

## Slide 16: Operation of the memory hierarchy
Register file
L1 (level 1) cache
L2 cache
L3 cache
Main memory
Disk(s) and/or SSD
Remote storage – remote in time
and/or location (e.g., the “Cloud”)
Copy/write arrows between levels are thinner at higher levels to show block size reduction necessary as access speed increases
Movement of bits between these hierarchy levels is managed entirely by hardware
Movement of bits in/out of this level managed by Operating System
Movement of bits between registers and L1 is by LOAD/STORE instructions
Movement of bits in/out of this level managed by various means
Transfer size = CPU register size
Transfer size = L1 block size
Transfer size = L2 block size
Transfer size = L3 block size
Transfer size = Page size
Transfer size = K bytes

## Slide 17: The Block
The “chunk of bits” that moves between to adjacent levels is called a block, generically
For efficiency, block size is a power of 2 multiple of the size of a processor register
Block size is larger lower in the hierarchy
Blocks have different common names because the memory hierarchy developed over may years: cache line, main memory page, …

## Slide 18: Three Rules of the memory hierarchy
The lowest level in the hierarchy is the ultimate repository for all information long-term
A level above is provided a copy of information from the level below when the level above cannot satisfy a processor request
When the processor stores (writes information into the top level), that change must eventually propagate down the levels to maintain Rule 1. (Propagation is transparent to user programs.)

## Slide 19: Four key hierarchy design questions
Q1: Where can a block be placed?
Q2: How is a block found?
Q3: Which block should be replaced on a miss?
Q4: What happens on a write?
These questions nicely map out the design space for memory hierarchy
The answers to these design quesitons affect hardware performance and inform software best practices

## Slide 20: Caching
Key concept in computing
Used in both hardware and software
Memory caching can strongly reduce the Von Neumann bottleneck by reducing the time spent making memory accesses

## Slide 21: Cache characteristics
Fast: the characteristic of principle interest
Small: the unavoidable characteristic; likely cannot hold every desirable item
Active: uses simple, fast hardware to make decisions about which items to store
Transparent: invisible to both requestor (say, CPU) and the slower, larger memory
Automatic: operation is entirely controlled by the sequence of addresses accessed and the access type (read, write)

## Slide 22: Cache operation
CPU executes fetch, LOAD, or STORE, sending an address to cache; cache searches using address, then either
  HIT: cache has a copy of the bit string in main memory and fetch/LOAD/STORE is processed on this copy, or
  MISS: cache does not have a copy of the bit string; must remedy this deficiency, then process fetch/LOAD/STORE
HIT and MISS occur with a measurable average frequency, or rate, for a program
HIT and MISS each take a typically fixed amount of time: hit time and miss penalty

## Slide 23: Memory hierarchy performance equations
Average memory access time model = Hit rate x Hit time + Miss rate x Miss Penalty = r Ch + (1-r)Cm
Memory request goes both to cache and to “large data storage”; if HIT then cancel request to storage, else wait for storage to process the request

## Slide 24: Simple cache idea
X4 |  | X4
X1 |  | X1
Xn-2 |  | Xn-2
Xn-1 |  | Xn-1
X2 |  | X2
 |  | Xn
X3 |  | x3
Cache before
reference to Xn
Cache after
reference to Xn
Reference to Xn causes a cache miss that forces the cache hardware to fetch Xn from memory and insert it into the cache.
Cache: a small, fast memory

## Slide 25: How do we find an item in cache?
One answer: Design exactly one place in the cache for each word in memory; called direct mapped
Memory access is frequent; so Amdahl’s Law says the mapping should be very fast, so use
  (Memory block address) mod (cache size in blocks)
  where # cache blocks = 2k so that mod function is just the low-order log2(cache size in blocks) bits of memory block address
Cache block size is a power of 2 number of consecutive memory locations; that number chosen to enhance memory performance

## Slide 26: Cache addressing example, 32-bit address
Let cache have 1024 blocks each containing 4 32-bit words, thus
  Index (pointer to a block) requires 10 bits
  Byte offset (pointer to one byte within a block) requires 4 bits
  Tag field gets all remaining bits
31 30 … 15 14 13 … 5 4 3 2 1 0
Tag
Index
Byte offset
Address fields (showing bit positions) of this cache

## Slide 27: 1024-block direct-mapped cache with 4-word blocks

## Slide 28: Is this the item we are looking for?
A location in memory is uniquely identified by its address
Only low-order address bits are used to place item in cache, so use high-order bits to tag each block, yielding a unique combination
Corner case: cache start up. Need to recognize when cache contents are meaningless; add valid bit
111
110
101
100
011
010
001
000
TAG
TAG
TAG
TAG
TAG
TAG
TAG
TAG
V
V
V
V
V
V
V
V

## Slide 29: Algorithm for direct-mapped cache access
Given: a memory address, A
Function: access word at address A
Method:
  Extract tag t, index b, and offset o from fields in address A
  If ( tag at block b matches t && Valid_bit == true) {
    Use o to select word and deliver to CPU } Else { /* update cache block destroying current block contents */ Fetch block containing address A from some level below Write block in cache slot b /* overwrites existing content */ Set tag of slot b to t Set Valid=true Use o to select word within block and deliver to CPU }

## Slide 30: Cache operation example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
Initial state of cache after power on.

## Slide 31: Cache operation example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | (Contents not valid, so MISS; bring in data from memory)
111 | N |  | 
Try to access address (10110two) but cache MISS.

## Slide 32: Cache operation example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10two | Memory (10110two)
111 | N |  | 
After MISS of address (10110two) due to NOT VALID.

## Slide 33: Cache operation example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | (Also a not valid block; MISS; bring in data)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10two | Memory (10110two)
111 | N |  | 
Try to access address (11010two) but again not valid miss.

## Slide 34: Cache operation example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11two | Memory (11011two)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10two | Memory (10110two)
111 | N |  | 
After handling a miss of address (11010two).

## Slide 35: Cache operation example
Index | V | Tag | Data
000 | Y | 10two | Memory (10000two)
001 | N |  | 
010 | Y | 11two | Memory (11011two)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10two | Memory (10110two)
111 | N |  | 
After handling a miss of address (10000two).

## Slide 36: Cache operation example
Index | V | Tag | Data
000 | Y | 10two | Memory (10000two)
001 | N |  | 
010 | Y | 11two | Memory (11011two)
011 | Y | 00two | Memory (00011two)
100 | N |  | 
101 | N |  | 
110 | Y | 10two | Memory (10110two)
111 | N |  | 
After handling a miss of address (00011two).

## Slide 37: Cache operation example
Index | V | Tag | Data
000 | Y | 10two | Memory (10000two)
001 | N |  | 
010 | Y | 11two | Memory (11011two)
011 | Y | 00two | Memory (00011two)
100 | N |  | 
101 | N |  | 
110 | Y | 10two | Memory (10110two)
111 | N |  | 
Now address (10010two); block is valid but tag MISMATCH.

## Slide 38: Cache operation example
Index | V | Tag | Data
000 | Y | 10two | Memory (10000two)
001 | N |  | 
010 | Y | 10two | Memory (10010two)
011 | Y | 00two | Memory (00011two)
100 | N |  | 
101 | N |  | 
110 | Y | 10two | Memory (10110two)
111 | N |  | 
Now address (10010two); replace block contents with
that of address (10010two).

## Slide 39: Improving cache performance
Cache performance model is embodied by Average memory access time = Hit time + Miss rate x Miss penalty
Cache optimizations can usefully be organized according to which term and/or factor of the average_memory_access_time is improved
  Reducing the miss rate
  Reducing the miss penalty
  Reducing the time to hit
Using models, using math, to formally describe a system helps avoid overlooking ways to improve
Supports “Never, …, never give up!” design strategy

## Slide 40: Instruction and data cache designs
Instruction accesses mostly sequential
  Default_next_instr._addr. is the most common because branch/jump/jsr instructions a minority
  Prefetching along the default path pays off nicely
Data accesses less predictable
  Less locality of reference
  Prefetching payoff is less
Small cache size accentuates these differences
Cache designs should be evaluated by testing on actual workloads when possible

## Slide 41: Memory hierarchy split and addressing
L1 Instr. cache
L2 Instr. cache
Unified Instr. & Data L3 cache (von Neumann)
Unified main memory
Unified local disk(s) and/or SSD
Unified remote storage, remote in time (a massive and slow technology) and/or spatial location (the “Cloud”)
L1 Data cache
L2 Data cache
Unified Instr. & Data L3 cache (von Neumann)
Unified main memory
Unified local disk(s) and/or SSD
Unified remote storage, remote in time (a massive and slow technology) and/or spatial location (the “Cloud”)
IF
stage
MEM
stage
Addressed using
Reg name
Memory address
Inode, URL, etc.

## Slide 42: Cache size
Experiments show cache hit ratio increases with increase in cache size
But also costs of hit (access time) and cost of miss tend to increase with cache size
Also, some programs have great hit ratios with small cache, some need big cache to get good hit ratios
Conclusion: experiments are helpful essential

## Slide 43: Improving cache performance
Block is the unit of information transferred between levels in the hierarchy
Moving a consecutive multiword block often takes same time as 1 word; parallelism
Reading from the memory hierarchy is easy; writing is harder
  Hierarchy Rules 1 & 2 “bubble up” information to faster levels, so reads access faster levels
  Rule 1 demands that writes access the slowest level, a serious obstacle to performance
  Rule 3 crucial to making writes faster

## Slide 44: How to handle writes with caching
Write-through strategy: CPU writes into the cache and the write continues through the cache to the lowest level of the hierarchy
  Satisfy Rule 3 of the Memory Hierarchy right now
  Costs right now the time to write to a slow level; likely stalls CPU
Write-back strategy: CPU writes into cache now. Later when forced to do so, the cache writes down a level, and so on
  Write-back strategy procrastinates on satisfying Rule 3
  Writes complete at the speed of the cache, like reads
  Push off cost of writing to the slow, low level as far into the future as possible; CPU not involved, so no direct CPU stall
  Can “absorb” several writes to one cache block that are written back as a single operation, eventually, saving costs that multiple write-through actions would incur
  Must write program output to lowest level, else program fails

## Slide 45: Writing changes later- Write Back
Must mark changes as you go
  At minimum requires a single bit for each cache block (could label at finer granularity)
  Traditionally this bit is called the dirty bit
When a cache miss will force replacement of of a dirty block, that block must first be written back (to the next lower memory level)
Enforces Rule 3 of the Memory Hierarchy per its “eventually” clause

## Slide 46: Write-back cache with 4-word blocks

## Slide 47: Set-associative cache
When cache maps any block to 1 place, then memory accesses with same index but different tags conflict in cache block with their index
Revise circuit to let each index hold more than 1 block, called a set-associative cache
When a new block is to be brought in to full set there is now a choice of which block currently in the set to replace
Must include a circuit to make this choice fast

## Slide 48: Make this cache 3-way associative

## Slide 49: Make cache bigger via associativity
Example, replicate storage area 3x so each block has 3 available placements
  Why number of placements != 2k ? Associative storage areas are not separately addressed; they are only tag matched
  3-way associative requires 3 tag match circuits, , not 1
VDTag Data
=
=
=
=

## Slide 50: Fully associative cache, no conflict
Compulsory miss reduction is limited by how wide an interface a given memory technology supports
Capacity miss reduction limited by affordability of a larger cache (circuit $ and heat factors)
Conflict misses can be avoided (eliminated) by a design that lets any block be placed anywhere in cache
  Corresponds to an Index field of zero bits; only have tag field and offset field
Use fully associative cache when
  Miss penalty is huge, and
  Can afford the time to agonize over which block to replace when, not if, that time comes

## Slide 51: Disadvantage of associative cache
Must make a choice when replacing a block
To achieve acceptable speed choice-making by hardware is required
What algorithm should circuit implement?
  Optimal choice is to replace that block in the set having its next use farthest into the future (delay paying the cost of re-loading a block into cache as much as possible)
  Optimal choice is a tough algorithm even for software, certainly problematic for hardware

## Slide 52: More practical replacement algorithms
Least recently used (LRU) uses measurable past as a proxy for prediction of the future
  “Least” easy to track in hardware for sets with just 2 blocks, but much harder for >2 blocks per set
Try approximation algorithms instead, such as
  Not Recently Used (NRU)
    Add a “Referenced” bit to each cache block; clear all such bits periodically, then set whenever a block is referenced (used)
    Replace block with lowest category value in this table
Block category | Referenced? | Dirty?
3 | Y | Y
2 | Y | N
1 | N | Y
0 | N | N
Don’t forget the hardware for tie-breaker capability
Notes:   To do LRU for more than 2, we must build a ranked list purely in hardware.
  Circuit gets big and slow fast :^)

## Slide 53: More thoughts
Two more “easier” (fast) algorithms
  First-in, first-out
  Pseudo-random (!)
All algorithms can work well at times, and all can fail totally at times
Simulation on real workloads is valuable to designers
Cache-aware compiling for a given platform can deliver performance value
Your complete computing platform determines your experience

## Slide 54: The 3 C’s of cache miss categories
Miss categories
  Compulsory miss (also called cold-start miss or first-reference miss): name for the miss that must occur on the first access to a block
  Capacity miss: misses caused because cache cannot hold all blocks ever accessed by a program
  Conflict miss: if there is any restriction on where a block can be placed in cache, then in addition to compulsory and capacity misses, conflict misses occur when too many accessed blocks map to the same cache location
3 C’s provide helpful guidance for cache designers seeking to improve performance by reducing misses

## Slide 55: Playing in the cache design space
Increase/decrease (in/de) size of offset field
  Increase/decrease words in block, so decrease/increase compulsory misses to extent accesses are sequential-ish
  Increase hardware interface between cache and both CPU and memory
In/de (size of index field + size of offset field)
  In/de total cache size, so de/in capacity misses & in/de cache cost
  In/de cache circuit size which in/de access time
Increase/decrease cache associativity
  Decrease/increase conflict misses
  In/de cache circuit size & in/de access time

## Slide 56: Summary
Caching is a fundamental performance technique
Large design space with many optimization techniques
Simulation guides design quantitatively
For programmers to maximize caching benefit
  Group related data items into adjacent blocks
  Perform all operations on a data item before moving on to another data item