## Slide 1: Lecture 20 – Operand addressing
2017.10.06
People have no memory of phone numbers now because of the cell phone - their address book is in a cell phone.
– Gordon Bell
Led development of the VAX computer

## Slide 2: Assignment for today
Finish reading chapter 7
Read chapter 8

## Slide 3: Announcements
Lab sessions cancelled next week (Oct. 11-13)
Optional Lab 04B posted on Blackboard
  Lab 04B is a register with LOAD, INVERT, and CLEAR
  You may replace your existing Lab 04 score with a score for Lab 04B by submitting work for Lab 04B
  Lab 04B is due the week of Oct. 16

## Slide 4: Early computers
Hardware was strongly quantity limited because
  Cost per gate was high
  Reliability of gates was low
    Circuits with more than, say, a few thousand gates would likely contain a faulty gate
Computers were unfamiliar, hence used by a small community
Thus
  Circuitry to execute instructions and to store useful amounts of instructions and data kept to a minimum
  Users could be trusted with the whole system and were willing to deal with its lack of built in support for many things

## Slide 5: Example: IBM 1401 circuit card

## Slide 6: Instruction operands: How few is possible?
Each operand requires bits for either its immediate value or a pointer to operand
Immediate values are fast, but not necessary, so consider only # of pointers
Number of pointers (# of addresses) used in the instructions of actual ISAs:
  Zero, called a 0-address architecture
  One, 1-address architecture
  Two, 2-address architecture
  Three, 3-address architecture

## Slide 7: 0-address architecture: Stack machine
Operand locations are always implied, except
PUSH and POP instrs. have explicit operands
  PUSH and POP move operands between memory and a stack (of registers) within the processor
Instructions other than PUSH and POP take operand(s) from the stack, starting at the top, and place result on the new top of the stack
Example of a stack machine: a Reverse Polish Notation (RPN) calculator

## Slide 8: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Memory
Push A
Push B
Add
Pop C
Push A
A
A
B
Assembly instruction PUSH copies the contents of a memory location into Top of Stack register.
PUSH A uses the pointer A to point at a memory location, where the contents, also called A, are copied to the top of the stack.

## Slide 9: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Push A
Push B
Add
Pop C
Memory
Push B
B
A
B
A
PUSH B copies B to the top of the stack.
A stack is a hardwired set of registers connected to perform the function of the stack data structure.
When an item is to be loaded into the stack Top position, all registers in the stack shift (load) their contents into the next lower register in the stack, making room at the TOP for the new item.
The number of registers in the Stack is a design choice.
If a stack is full, PUSH could drive the contents of the lowest stack register into the bit bucket – bad news for the program – so stacks include the ability to spill into memory.

## Slide 10: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Push A
Push B
Add
Pop C
Memory
Add
The ALU in a stack machine is hardwired to obtain two operands, one each from the Top of Stack register and the Next to Top register. Note the two arrows showing the paths from these registers to the ALU.
When the operation executes, the entire stack shifts its contents up one register level and the ALU output (operation result) is loaded into the Top register. Both operands in the stack are overwritten (bit bucket, again) as a side effect of execution, but copies remain in memory.
If the ALU operation is defined to use only one operand then the stack does not shift up and the result overwrites its own operand.
B
A
C
C
B
A

## Slide 11: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Push A
Push B
Add
Pop C
Memory
Pop C
C
B
A
Assembly instruction POP copies the contents of the Top of Stack register into a designated memory location AND causes the registers in the stack to all shift up a level, overwriting the current Top contents.
POP C uses the pointer C to point at a memory location and write into it the contents of Top of Stack, also called C.

## Slide 12: 1-address: Accumulator machine
One special register, called the accumulator
One operand for most instructions is the accumulator, one operand from a memory address
Result always sent to the accumulator; previous accumulator contents sent to the bit bucket
Example: cheap calculator

## Slide 13: 2-address machine
Not a stand-alone processor design
Rather, a design for an embedded memory copying circuit

## Slide 14: 3-address machine: current processors
Gain ability to specify location to store result
Avoid side effect of overwriting an operand
Machine code sequences to implement high-level language programs are more compact and faster
Register file is a design choice with the purpose of avoiding some use of slow main memory circuits

## Slide 15: Code for C=A+B for 0-, 1-, and 3-addr.
Assumes A, B, C all belong in memory and that A, B not destroyed
Reg-Reg/
Load-store
ALU
…
…
…
ALU
…
…
ALU
…
…
…
…
ALU
…
…
…
…
Processor
Top of
Stack 
Stack
Accumulator
Reg-Mem
Stack
Accum-ulator
Reg file
Reg file
Push A
Push B
Add
Pop C
Load A
Add B
Store C
Load R1,A
Add R4,R1,B
Store C,R4
Load R1,A
Load R2,B
Add R4,R2,R1
Store C,R4
Memory
C
B
A
C
B
A
C
B
A
C
B
A

## Slide 16: ISAs with dedicated instr. for mem access
0-address and Reg-Reg, a.k.a Load/Store, architectures have instructions specifically to read/write computer memory
3-address
Reg-Mem
Architecture
3-address
Reg-Reg/
Load-store Arch.
ALU
…
…
…
ALU
…
…
ALU
…
…
…
…
ALU
…
…
…
…
Processor
Top of
Stack
Memory
0-address
Stack architecture
1-address
Accumulator
Stack
Accum-ulator
Reg file
Reg file
Push
Pop
Load
Store

## Slide 17: Sources of operands
Immediate operand – the field in the instruction bit string contains the actual bit string of the operand (the operand value)
  Called “immediate” because there is immediate access to the operand value for execution
Register – pointed to by an instruction field
Memory – a memory address is, typically, too many bits to fit within a field within an instr.
  Pointer to in-memory operand will be computed
  Memory is slow these days, so we source operands from memory only when we must

## Slide 18: Example operand addressing modes (Fig. 7.6)
Notes: Thought question

## Slide 19: Von Neumann bottleneck
Today, main memory technology (DRAM) is very slow compared to speed of a processor
  Processors consume operands and produce results far faster than current main memory technology can readily source and sink them
Time spent accessing memory often dominates the total time to run a program
Architects use the term von Neumann Bottleneck to describe the situation when memory access time (processor waiting) is the majority of the run time

## Slide 20: Design tradeoffs for operands
Different operand sources and forms have different
  Ease of programming/compiling
  Fewer/more machine instructions
  Smaller/larger machine instructions
  Larger/smaller range of immediate values
  Faster/slower operand fetch
  Larger/smaller processor circuit size
There is not one right answer

## Slide 21: Summary
Operand types and addressing are design choices
Immediate operands are constants contained within the instruction
Pointers to registers (smaller) and memory (often too large) are used in instructions
Can obtain operands via indirection
  Register contains an address to memory
  A memory location contains an address to memory

## Slide 22: Lecture 21 – Modes and Microcode
2017.10.06
It’s a small world after all.
– Walt Disney

## Slide 23: Assignment for today
Finish reading chapter 8
Read chapter 10 and 11 about memory

## Slide 24: Anouncements
This slide intentionally left almost blank

## Slide 25: Execution modes
CPU hardware has several possible modes
At any time, CPU operates in one mode
Mode sets various parameters, including, but not limited to
  Privilege level
  Which instructions of the ISA are valid
  Which addresses are valid
  Size of data items
  Backward compatibility with earlier ISAs

## Slide 26: How to think about modes
Imagine different CPUs inside a given CPU
Mode selects which CPU is currently in use
Two modes may have different
  Numbers of registers
  Register size
  Instruction sets

## Slide 27: How to change between modes
Automatic change (hardware does its thing)
  Initiated by hardware: example, an Input/Output (I/O) device needs service
  Prior to changing mode, operating system (OS) specifies the new mode
“Manual” change (under program control)
  Initiated by software, typically the OS
  Typical example, application program calls an OS function
  Some modes can be selected by an application

## Slide 28: Privilege and protection
Number of privilege levels is a design choice: from 0 levels up to 8 levels have been built
Levels limit operations allowed so CPU can detect “unauthorized operations”
Example, I/O device service (printing)
  CPU must allow device driver software in the OS to interact with the I/O device
  Applications must not be allowed to do this
    Erroneous or malicious commands to I/O devices are often dangerous
Notes: Halt and Catch Fire story here

## Slide 29: Microcoded instructions
How should a CPU be implemented?
One way is totally in hardware, another is to combine a simpler circuit and stored code
  Microprocessor (simple, perhaps narrow circuit) provides basic instructions
  Stored code implements “macro” instructions built out of basic instructions and offers additional, more sophisticated capabilities
Key idea: can add complex instructions (macro) more easily via code than via circuitry
  Change stored code to allow field upgrades

## Slide 30: CPU with microcode

## Slide 31: 32-bit ADD32 macro for 16-bit circuit
Figure 8.4
01
02
03
04
05
06
07
08
09
10
11

## Slide 32: Microcode pro and con
Pro
  Fast update (revision) of a processor
  Circuit errors possibly can be “papered over” by adding microcode to compensate for a flaw
  Microcode usually hidden from programmers
Con
  Execution time: macro instructions take the time of multiple machine instrs. (microcode instr.)
  Microcode usually hidden from programmers; when not hidden, CPU is called “reconfigurable”

## Slide 33: Vertical or horizontal microcode
Vertical microcode uses a full-featured, but simpler and/or narrower microcontroller and then builds macro instrs. on this foundation
  Example, x86 uses a RISC microcontroller inside and vertical microcode to implement CISC instructions of x86 ISA
  One macro instruction usually requires several to many micro-instructions
Horizontal microcode, in contrast, specifies control signals for processor function units: no decode for horizontal micro-instructions

## Slide 34: Horizontal microcode format
Horizontal microcode is programming the control signals for a processor, Figure 8.5, for example
One data path shared by all units, rather than dedicated paths as seen in Fig. 6.9

## Slide 35: Implementing horizontal microcode
Fig 8.9: code to add
Each machine language instruction will have a microcode sequence similar to the above
Executing a machine language instruction is like calling a subroutine
Each horizontal microcode sequence needs HALT or RETURN; may also need conditional execution and iteration capability; above figure does not show this

## Slide 36: Horizontal microcode characteristics
Easy to specify simultaneous, Parallel, operation of processor hardware units
Example: an ALU operation that takes more than one clock cycle to complete
  Operands finish coming from fast register unit during the first clock cycle
  Register unit could then sit idle, or instead, could perhaps service other operations while multi-cycle ALU operation continues to execute
  More work in progress simultaneously means overall work of a program may complete sooner

## Slide 37: Summary
CPU modes determine protection and privilege
CISC ISA usually implemented with vertical microcode; RISC ISA usually no microcode
Vertical microcode uses a conventional- looking code (like assembly for a simpler CPU)
Horizontal microcode looks like complex Boolean logic functions
Horizontal microcode, when used, is for the purpose of achieving more simultaneous circuit actions to advance program progress