## Slide 1: CS250 Lecture 40 – Parallel computers
2017.11.29
E pluribus unum.

## Slide 2: Announcements
Lecture today covers chapter 18

## Slide 3: Announcement
Course evaluation survey is now open
  I welcome your comments and will use them to improve the course
  Thank you for paying it forward to CS students

## Slide 4: Some next steps to increase parallelism
Examples of parallelism covered so far
  Larger CPU word size: process more bits per clock
  Pipelining CPU: overlap instruction processing
  Multiple memory modules: increase throughput
Advanced ideas, one example
  Have IF and ID stages fetch, decode, and issue multiple instructions simultaneously, example
    Fetch all instructions in a i-cache block simultaneously
    Decode, analyze for dependence, rename registers to eliminate anti- and output dependences, then
    Send to EX all instructions that do not violate a true data dependence nor cause a structural hazard (and, while we are at it, use Moore’s Law to add more ALU, MEM, and WB hardware to reduce incidence of structural hazards)

## Slide 5: Parallel computers
Parallel computer term used when parallelism dominates the entire architecture
Employ a “team” of processors to increase performance for large computational tasks
Challenges, two main questions
  How to decompose the overall computation into a set of tasks for the set of processors?
  How to coordinate the work of the “team”?

## Slide 6: Decomposition and data dependences
Calculations that depend on prior calculations must be executed in program order
No program can run more quickly than its longest chain of dependent calculations, known as the critical path
However, most algorithms do not consist of just one long chain of dependent calculations; there are usually opportunities to execute independent calculations in parallel

## Slide 7: Categorization by cost of coordination
Fine-grain parallelism: communication between tasks is frequent
  Issuing multiple instructions per clock cycle is fine grain parallelism because each instruction computes a result that likely is read by an instruction following closely within the program
Coarse-grain parallelism: communication between parallel tasks is infrequent
Embarrassingly parallel: communication between parallel tasks is rare or never occurs

## Slide 8: Flynn parallel architecture taxonomy
Classify programs and computers by number of instruction streams and number of data streams
SISD (Single Instruction stream/Single Data stream): the classic sequential computer
SIMD (Single Instruction stream/Multiple-Data streams): each instruction applied simultaneously to multiple elements of a data set; the typical GPU
MISD (Multiple-Instruction streams/Single-data stream): rare; seen in fault-tolerant, critical computing applications
MIMD (Multiple-Instruction streams/Multiple-data streams): high-performance cluster computers
Some computers are hybrids of the above, some do not neatly fit in, but this simple scheme gives a useful first approximation
Notes: Taxonomy: a scheme of classification

## Slide 9: SIMD details
Control Unit (CU) contains IF and ID stages and instruction memory
Processing Elements (PEs) each contain EX/MEM/WB stages and data memory
CU fetches, decodes, and broadcasts decoded instructions to PEs: single instruction stream sent from CU to all PEs
PEs execute instructions using their locally stored data: multiple data streams, one per PE
Straight line code execution looks similar to SISD
Program structures with conditional execution – if ( ) { } and while ( ) { } – require special handling

## Slide 10: SIMD machine diagram: CU and PEs
CU fetches, decodes, and broadcasts machine instructions to all PEs
PEs always execute control-type instructions, but top bit of each PE Enable Stack controls execution of non-control-type instructions
Top==TRUE then PE executes; Top==FALSE, PE ignores CU broadcast instr.
EX / MEM / WB stages
Data Memory 0
Processing Element 0
Enable Stack (1 bit wide)
Control Unit
Instruction Memory
IF / ID stages
• • •
• • •
Instruction broadcast bus
EX / MEM / WB stages
Data Memory N-1
Processing Element N-1
Enable Stack (1 bit wide)

## Slide 11: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.

## Slide 12: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.
if ( A ) { if ( B ) {
C ;
} else {
D ;
} } else {
E ;
} F ;

## Slide 13: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.
if ( A ) { if ( B ) {
C ; // Non-control-type instruction; tell a PE what computation to do
} else {
D ; // More generic computational work; CU broadcasts machine code
} } else {
E ; // CU broadcasts sequence of machine code instructions
} F ; // CU again fetching, decoding, and broadcasting machine instruction(s)

## Slide 14: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.
if ( A ) { // Control instruction. CU broadcasts instrs. to load all PE Enable Stacks:
// Push 2 bits onto each enable stack to control the two parts of an if-else // For if without else push 1 bit if ( B ) {
C ;
} else {
D ;
} } else {
E ;
} F ;

## Slide 15: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.
if ( A ) { // Control instruction. CU broadcasts instrs. to load all PE Enable Stacks:
// Push 2 bits onto each enable stack to control the two parts of an if-else // For if without else push 1 bit if ( B ) { // Control instruction: Push 2 bits onto each enable stack for if-else
C ;
} else { // Control instr.: Pop bit controlling if body instrs. C from each enable stack
D ;
} } else {
E ;
} F ;

## Slide 16: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.
if ( A ) { // Control instruction. CU broadcasts instrs. to load all PE Enable Stacks:
// Push 2 bits onto each enable stack to control the two parts of an if-else // For if without else push 1 bit if ( B ) { // Control instruction: Push 2 bits onto each enable stack for if-else
C ;
} else { // Control instr.: Pop bit controlling if body instrs. C from each enable stack
D ;
} // Control instruction (Quelle surprise!)
// Pop bit controlling else instructions D } else {
E ;
}
F ;

## Slide 17: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.
if ( A ) { // Control instruction. CU broadcasts instrs. to load all PE Enable Stacks:
// Push 2 bits onto each enable stack to control the two parts of an if-else // For if without else push 1 bit
if ( B ) { // Control instruction: Push 2 bits onto each enable stack for if-else
C ;
} else { // Control instr.: Pop bit controlling if body instrs. C from each enable stack
D ;
} // Control instruction (Quelle surprise!)
// Pop bit controlling else instructions D } else { // Control instruction: Pop bit controlling if instruction block
E ;
} // Control instruction: Pop bit controlling else instructions E
F ;

## Slide 18: SIMD execution example: Nested conditionals
// Each PE has part of the entire data set available locally (multiple data streams) and
// a local, 1-bit-wide Processor_Enable_Stack where the top bit determines
// whether the PE executes non-control instructions broadcast by the Control Unit.
if ( A ) { // Control instruction; CU broadcasts instrs. to load all PE Enable Stacks:
// Push 2 bits onto each enable stack to control the two parts of an if-else // For if without else push 1 bit if ( B ) { // Control instruction: Push 2 bits onto each enable stack for if-else
C ;
} else { // Control instr.: Pop bit controlling if body instrs. C from each enable stack
D ;
} // Control instruction (Quelle surprise!)
// Pop bit controlling else instructions D } else { // Control instruction: Pop bit controlling if instruction block
E ;
} // Control instruction: Pop bit controlling else instructions E
F ; // Enable stacks all again same as before if (A) { } else { } statement

## Slide 19: SIMD execution example: What CU broadcasts

## Slide 20: SIMD execution example: What CU broadcasts
// Push* pushes the else condition, <condition_expression>’•T , where T is the current // top bit of the PE enable stack. If top bit = TRUE, then PE executes conditional code.
// Push** pushes <condition_expression>•T by reaching one position below stack top.

## Slide 21: SIMD execution example: What CU broadcasts
// Push* pushes the else condition, <condition_expression>’•T , where T is the current
// top bit of the PE enable stack. If top bit == TRUE, then PE executes conditional code.
// Push** pushes <condition_expression>•T by reaching one position below stack top
if ( A ) { // Let T be the truth value at the top of the enable stack at this time.
// CU broadcasts these two instructions for all PEs to execute:
// Push* A’•T  AND A’ with current top of enable stack // Push** A•T  Reach down into stack to AND with T again if ( B ) { // Push* B’•(A•T)  (A•T) is the new top of enable stack
// Push** B•(A•T)
C ; // Machine instrs. PEs with B•(A•T)==TRUE execute, other PEs ignore CU
} else { // Pop  PE enable stack top bit now B’•(A•T)
D ; // Machine instrs. PEs with B’•(A•T)==TRUE execute, other PEs ignore CU
} // Pop  PE enable stack top bit is now A•T // no machine instructions for CU to broadcast } else { // Pop  PE enable stack top bit is now A’•T
E ; // Machine instrs.  PEs with A’•T==TRUE execute, other PEs ignore CU
} // Pop  PE enable stack top bit is now T
F ; // Machine instrs.  PEs with T==TRUE execute, other PEs ignore CU

## Slide 22: Enable stack lets each PE simulate conditional branch
Push* pushes <condition>’•T ; Push** after a Push* pushes <condition>•T by reaching one position below current stack top to obtain correct context for if ( ) { }
Instructions Which PE enable stack
Control Unit PEs Top  deeper into stack
Broadcasts execute? Stack contents after instr. executes
if (A) { All T  T=initial top; evaluate A
Push* All A’•T T  A known; Push* A’ and T
Push** All A•T A’•T T  Push** A and T on stack
if (B) { All A•T A’•T T  evaluate B
Push* All B’•(A•T) A•T A’•T T  Push* B’•(current top)
Push** All B•(A•T) B’•(A•T) A•T A’•T T
C ; Enabled B•(A•T) B’•(A•T) A•T A’•T T  Enabled if B•(A•T)==TRUE
Pop All B’•(A•T) A•T A’•T T  Pop signals end if
D ; Enabled B’•(A•T) A•T A’•T T
Pop All A•T A’•T T  Pop signals end else
Pop All A’•T T  Pop signals end if
E ; Enabled A’•T T
Pop All T  Pop signals end else

## Slide 23: SIMD example
Graphics processors follow the SIMD design
Technique
  Divide image or video frame into many parts
  Send each image part to an identical graphic processor unit circuit where an identical algorithm is applied to the image subset data

## Slide 24: MIMD details
MIMD has multiple physical processors of SISD (typical) or SIMD (uncommon) category
Each processor
  Fetch-Executes its own program
  May have dedicated I/O devices (e.g., its own disk)
Parallelism is visible to the programmer
Use when computation can be decomposed into fairly independent (modest need for communication to coordinate) pieces

## Slide 25: MIMD machine diagram
Processor memories store programs and data; may be different for each
Processors fetch and execute their own instructions; communicate with other processors as software directs (explicit parallelism)
Coordinator helps implement BARRIERS, which synchronize processors
Interconnection network for data communication among processors
All pipeline stages
Memory 0
Processor 0
Coordinator (barriers)
• • •
All pipeline stages
Memory N-1
Processor N-1
Interconnection network (processor-to-processor communication)

## Slide 26: SIMD-MIMD comparison
SIMD
  Programs slightly more difficult to write than SISD
  Only one copy of program in memory
  No synchronization overhead
  Some algorithms will be very inefficient on SIMD
  If-then-else and while loops are interesting
MIMD
  Program much more difficult to write than SISD
  Copy of program in each processor
  Explicit synchronization required (barriers)
  Execute if-then-else constructs fully in parallel
  While loops are not harder to execute

## Slide 27: SISD-MIMD-SIMD run-time comparison
Straight line code: statements S1; S2; and S3;
SISD
MIMD
SIMD
Execution traces for
S3;
S1;
S2;
S3;
S1;
S2;
S3;
S1;
S2;
• • •
• • •
• • •
CU
S1;
S1;
• • •
S2;
S2;
• • •
CU
S3;
S3;
• • •
CU
CU
Fetch
Execute
Fetch
Execute
Fetch
Execute
Fetch
Execute
Fetch
Execute
Fetch
Execute

## Slide 28: SISD-MIMD-SIMD run-time comparison
if (A) { B; } else { C; }
SISD
MIMD
SIMD
Execution traces for
A?
False
True
C;
B;
A?
False
True
C;
B;
A?
False
True
C;
B;
A?
False
True
C;
B;
• • •
• • •
A?
Push** A
Push* A’
B;
Pop
C;
Pop

## Slide 29: SISD-MIMD-SIMD run-time comparison
while (A) { L; }
SISD
MIMD
Execution traces for
A?
False
True
L;
A?
False
True
L;
A?
False
True
L;
A?
False
True
L;
• • •
• • •

## Slide 30: SISD-MIMD-SIMD run-time comparison
while (A) { L; } //if fixed # iterations, let SIMD CU perform loop count
SISD (for comparison)
SIMD (fixed # of iterations)
Execution traces for
CU
L0;
L1;
L0;
L1;
• • •
• • •
• • •
CU
Ln;
Ln;
• • •
CU
A?
False
True
L;
Initial loop count
Loop count +1
Loop count =n

## Slide 31: SISD-MIMD-SIMD run-time comparison
while (A) { L; } // assume data-dependent number of iterations
data-dependent # of iterations
Execution trace for SIMD with
Each PE must individually evaluate A on its local data and determine if another loop iteration is needed.
If a PE evaluates A == True, then the PE reports that to the CU, which requests that a loop iteration be broadcast. The CU will
Push* A on all PE enable stacks, broadcast the loop body instructions, L, Pop the PE enable stacks, broadcast the instructions for A, and then examine the PE reports to determine if another iteration is necessary.
A?
Push* A
L;
Pop
Any PEs report true to CU?
Yes
No